## Slide 1: Reconfigurable Hardware
Professor Ryan Kastner
Dept. of Computer Science and Engineering
University of California, San Diego

## Slide 2: Reconfigurable Hardware

## Slide 3
Reconfigurable Hardware
  Main Entry: re-
  Function: prefix
  1 : again : anew <retell>
  2 : back : backward <recall>
Main Entry: con·fig·ure
Pronunciation: k&n-'fi-gy&r
Function: transitive verb
: to set up for operation especially
in a particular way
KEY ADVANTAGE: Performance of Hardware, Flexibility of Software
CLB
Block RAM
IP Core (Multiplier)

## Slide 4: Origins of Reconfigurable Computing
Fixed-Plus-Variable (F+V) Structure Computer
  Standard processor augmented with inventory of reconfigurable building blocks
  “… to permit computations which are beyond the capabilities of present systems by providing an inventory of high speed substructures and rules for interconnecting them such that the entire system may be temporarily distorted into a problem oriented special purpose computer.” - G. Estrin

## Slide 5: History of Reconfigurable Computing
Early Years – PLA, PAL
  One time programmable
  Programmed by blowing fuses
Complex Logic Devices
  FPGA, CPLD
  Reprogrammable (SRAM)
  Initially used for glue logic, ASIC prototyping
PLA
“Moore” transistors = more complex devices

## Slide 6: Modern Reconfigurable Devices
Reconfigurable devices are extremely complicated, multiprocessing computing systems
  Mix of hardware and software components
    Microprocessors – RISC, DSP, network, …
    Logic level (FPGA) Reconfigurable logic
  Specs for high end Xilinx Virtex 7
    1 GHz ARM Dual Core Cortex A9
    96 transceivers @ 28.05 Gb/s peak
    3600 DSP Slices @ 5,335 GMAC/s
    1,955K logic cells
    68 Mb BRAM
    1,200 I/Os
Can implement complex applications

## Slide 7: Traditional Choice: Hardware vs. Software
Properties of Hardware
  Fast: High performance
    Spatial execution
    Adaptable parallelism
  Compact: Silicon area efficient
    Operations tailored to application
    Simple control
    Direct wire connections between operations
Hardware Inflexible: Fixed at Fabrication
Source: DeHon/Wawrzynek

## Slide 8: Traditional Choice: Hardware vs. Software
Software Flexible: Fixed at Runtime
Properties of Software
  Slow:
    Sequential execution
    Overhead of interpreting instructions
  Area inefficient:
    Fixed width, general operators
    Area overhead
      Instruction cache
      Control circuitry
Souce: DeHon/Wawrzynek

## Slide 9: Reconfigurable Hardware
Fast:
  Spatial parallelism (like hardware)
  Application specific operators, control circuitry
Flexible:
  Operators and interconnect programmable (like software)
Source: DeHon/Wawrzynek

## Slide 10: Reconfigurable Hardware
Fast and flexible, but…
  Area overhead – switches, configuration bits
  Delay overhead – switches, logic
  Compilation
    Difficult - architecture “too” flexible
    Slow - based on hardware synthesis techniques
Source: DeHon/Wawrzynek

## Slide 11: Performance Benefits
Up to 100x performance increase compared to processors (microprocessor, DSP)
~10x performance density advantage over processors
Applications like:
  Pattern matching
  Data encryption
  Data compression
  Digital communications
  Video and image processing
  Boolean satisfiability
  Networking
  Cryptography

## Slide 12: Programmability Abstractions
Logic Level
ADD
Register
MUL
Control
Instruction Level
FU
Memory
Register
Bank
Control
Function Level
FU
Operands
Byte
Bit
Programming Unit
Functional Operation
Arithmetic Operation
Boolean Operation
(and, or, xor)
Basic Unit of Computation
Bus, Memory
Bundles of Wires, Registers
Wires, Flip Flops
Communication
Register
NAPA, RAW, RaPiD
PRISC, Chimaera, Garp
FPGA, CPLD
Example Devices
Flexibility
Performance
Power/Energy Consumption
Design Complexity

## Slide 13: Processor vs FPGA
Souce: DeHon

## Slide 14
FPGA
CLB
Switchbox
Routing
Channel
IOB
Routing
Channel
Configuration
Bit

## Slide 15
FPGA

## Slide 16: Programmable Logic
  Each logic element outputs one data bit
  Interconnect programmable between elements
  Interconnect tracks grouped into channels
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
Logic Element
Tracks

## Slide 17: Lookup Table (LUT)
Program configuration bits for required functionality
Computes “any” 2-input function
In Out
00 0
01 0
10 0
11 1
2-LUT
Configuration Bit 0
Configuration Bit 1
Configuration Bit 2
Configuration Bit 3
A
B
C
A
B
C=A  B

## Slide 18: Lookup Table (LUT)
K-LUT -- K input lookup table
Any function of K inputs by programming table
Load bits into table
  2N bits to describe functions
  => different functions

## Slide 19: Lookup Table (LUT)
K-LUT (typical k=4)
w/ optional
output Flip-Flop

## Slide 20: Lookup Table (LUT)
Single configuration bit for each:
  LUT bit
  Interconnect point/option
  Flip-flop select

## Slide 21: Configurable Logic Block (CLB)

## Slide 22: Programmable Interconnect
Interconnect architecture
  Fast local interconnect
  Horizontal and vertical lines of various lengths
C L
B
C L
B
C L
B
C L
B
C L
B
C L
B
Switch
Matrix
Switch Matrix

## Slide 23: Switchbox Operation
6 pass transistors per switchbox interconnect point
Pass transistors act as programmable switches
Pass transistor gates are driven by configuration memory cells
After Programming
Before Programming

## Slide 24: Programmable Interconnect

## Slide 25: Programmable Interconnect
25

## Slide 26: FPGA “Hardening”
FPGA-based reconfigurable devices
  Configurable logic blocks
    Flexible logic block
    Programmable interconnect
  Dedicated multipliers
  Embedded configurable block RAM
  RISC microprocessor cores
Other architectures
  Reconfigurable multi-core processor 
  Coarse-grained reconfigurable architectures 

## Slide 27: FPGA “Hardening”
Notes: Source: Xilinx Design documents
Fixed, fast multipliers
MAC, Shifters, counters
Hard/soft processor cores
  PowerPC
  Nios
  Microblaze
Memory
  Block RAM
  Various sizes and distributions

## Slide 28: Embedded RAM
Xilinx – Block RAM
  32k x 1 to 512 x 72 in one 36K block
  Simple dual-port and true dual-port configurations
  Built-in FIFO logic
  64-bit error correction coding per 36K block
  Adjacent blocks combine to 64K x 1 without extra logic
36
DIA
ADDRA
36
DOA
Port A
36 Kb Memory Array
CLKA
WEA
4
36
DIB
ADDRB
36
DOB
Port B
CLKB
WEB
4

## Slide 29: Embedded Functional Unit
Xilinx DSP48
  25x18 multiplier
  25-bit pre-adder
  Flexible pipeline
  Cascade in and out
  Carry in and out
  96-bit MACC
  SIMD support
  48-bit ALU
  Pattern detect
  17-bit shifter
  Dynamic operation (cycle by cycle)
Notes: Virtex 7 series DSP slice

## Slide 30: Xilinx 7 Series FPGAs
1 GHz ARM Dual Core Cortex A9
96 transceivers @ 28.05 Gb/s peak
3600 DSP Slices @ 5,335 GMAC/s
1,955K logic cells
68 Mb BRAM
1,200 I/Os
SelectIO
& CMT
Logic
DSP
Serial Transceiver
BRAM
Clock Buffers and Routing
PCI Express
SelectIO
& CMT
Notes: ARM for Zynq
Rest for highest end Virtex 7 (XC7V2000T)

## Slide 31: FPGA System Life Cycle
EDA Design Tools
Manufacturing Process
FPGA Device Vendors:
Altera, Xilinx
Foundry:
TSMC, UMC, SMIC
Manufacturing Stage
Memory
Memory
A/D
D/A
FPGA Board
System Developers:
Avnet, Digilent, NuHorizons, …
Deployment Stage:
Applications include military, transportation, banking and finance, SCADA, high performance computing, etc
Application Development Stage
FPGA
Codec
Physical Synthesis
Logic Synthesis
RTL Synthesis
System Synthesis
Intellectual Property (IP) Cores
Application Engineer using CAD tools developed by:
Cadence, Mentor Graphics, Synopsys, Mathworks, Altera, Xilinx
Specification:
C/C++, Matlab

## Slide 32: Tool Chains
Notes: There are many tools out there. Since most computer scientists are not experts at HDL design, tools are needed to translate algorithms into circuits.
HDL design is tricky. Many proposals for tools for high-performance computing applications that run on hybrid CPU/FPGA systems in which FPGAs handle the most intensive tasks (10%-90% rule).
How do we profile an FPGA application?

## Slide 33: Programming the FPGA
Configure logic – CLBs, LUTs, FFs
Configure interconnect – channel, switchbox
Large number of bits – 500 Mb
Configuration bit technology
  Antifuse (program once)
  SRAM
  Floating Gate (Flash)

## Slide 34: Antifuses
Opposite of fuse (open until blown)
Make a connection with electrical signal
  The current melts a thin insulating layer to form a thin permanent and resistive link.
  More reliable than breaking a connection (avoids shrapnel)
Permanently programmed (Non-volatile)
Notes: Metal–metal antifuse. (b) A metal–metal antifuse in a three-level metal process that uses contact plugs. The conductive link usually forms at the corner of the via where the electric field is highest during programming.

## Slide 35: Antifuses
Source: Actel

## Slide 36
Mode
(Read/Write)
Input Data
SRAM
Configuration
Bit
Output
SRAM
Volatile
6 CMOS transistors
Standard fabrication process
Notes: Configurable interconnect using a pass gate controlled by single SRAM configuration bit. If the SRAM bit is set, then A is electrically connected to B. Otherwise, A and B are not connected.

## Slide 37: Floating Gate (EPROM/EEPROM/Flash)
By applying proper programming voltages,
electrons “jump” onto floating gate
Electrons on gate raise threshold voltage so transistor always off
Flash switch is comprised of two transistors which share a gate
Notes: (a) With a high (>12V) programming voltage, VPP, applied to the drain, electrons gain
enough energy to “jump” onto the floating gate (gate1)
(b) Electrons stuck on gate1 raise the threshold voltage so that the transistor is always off
for normal operating voltages
(c) UV light provides enough energy for the electrons stuck on gate1 to “jump” back to the
bulk, allowing the transistor to operate normally

## Slide 38
SRAM Versus Flash Switch & Memory Size
SRAM based PLD
FLASH based PLD
Switch
& Routing
Memory
Cell
Switch
& Routing
Memory
Cell

## Slide 39: Programming Technology
 | SRAM | Antifuse | Flash
Speed | Medium | Fast | Slow
Power | Poor | Good | Good
Relative Size | 1 | 1/10 | 1/7
Reprogram | Yes | No | Yes
Size | Large | Small | Moderate
Volatile | Yes | No | No

## Slide 40: FPGA System Life Cycle
EDA Design Tools
Manufacturing Process
FPGA Device Vendors:
Altera, Xilinx
Foundry:
TSMC, UMC, SMIC
Manufacturing Stage
Memory
Memory
A/D
D/A
FPGA Board
System Developers:
Avnet, Digilent, NuHorizons, …
Deployment Stage:
Applications include military, transportation, banking and finance, SCADA, high performance computing, etc
Application Development Stage
FPGA
Codec
Physical Synthesis
Logic Synthesis
RTL Synthesis
System Synthesis
Intellectual Property (IP) Cores
Application Engineer using CAD tools developed by:
Cadence, Mentor Graphics, Synopsys, Mathworks, Altera, Xilinx
Specification:
C/C++, Matlab

## Slide 41: Tool Chains
Notes: There are many tools out there. Since most computer scientists are not experts at HDL design, tools are needed to translate algorithms into circuits.
HDL design is tricky. Many proposals for tools for high-performance computing applications that run on hybrid CPU/FPGA systems in which FPGAs handle the most intensive tasks (10%-90% rule).
How do we profile an FPGA application?