## Slide 1: Designing Robot Behaviors
Week #6
Prof. Ryan Kastner

## Slide 2: Designing Robot Behaviors
Be Creative
Recognize the Strengths and Limitations of the Robot
Know the environment the robot will be working in
Know available paradigms for programming robots behaviors

## Slide 3: Braitenberg Vehicles
Valentino Braitenberg wrote a book titled: Vehicles: Experiments in Synthetic Psychology (MIT Press)
Describes several thought experiments that are centered around the creation of simple vehicles with very simple control mechanisms that exhibit seemingly complex behavior
Illustrates insights into animal (human) brain
Shows that vehicles are capable of complex behavior like Fear, Love, Logic etc.

## Slide 4: Law of Uphill Analysis and Downhill Invention
One central theme underlying Braitenberg's experiments
Trying to postulate the internal structure purely by observing certain behavior is an uphill (harder) task
Trying to create an entity that exhibits a certain behavior is a downhill (easier) task
A Scribbler can do most of what the robots Braitenberg described can do

## Slide 5: Vehicle 1
Alive
  One Sensor – One Motor
Scribbler
  One Sensor – Two motors
You can use the center light sensor and connect what it reports directly to both motors of the robot
Try this:
    motors(c,c) where ‘c’ is the value from light sensor

## Slide 6: Movement Using Light Sensors
Light sensors report values in range of 0 – 5000 while motors take values from -1 to 1
Normalizing (mapping light sensor values to the range of motor values)
  def normalize(v): # normalizes v to range 0.0 to 1.0
  def main():
    while True:
      L = getLight("center")
      forward(normalize(L))

## Slide 7: Normalizing Sensor Values
Normalizing is transforming a value proportional to a required range (here 0.0 to 1.0, 1.0 being brighter light)
Light Sensor is actually a Darkness sensor
  Small values for bright light e.g. 50
  Larger values for dark light e.g. 3000
    def normalize(v):
    # Normalize v (in the range 0..5000) to 0..1.0, inversely
    return 1.0 - v/5000.0
  For brightness v = 35 what is the normalized value

## Slide 8: Light Sensing
You can set the ambient light value as the darkest condition so that you can identify a brighter light, say, a Flash Light
How:
    def normalize(v):
      if v > Ambient:
      v = Ambient
      return 1.0 - v/Ambient
Either you can set this value or let the Robot sense it
You can also find the values sensed by left and right sensors and take an average

## Slide 9: Coward and Aggressive
Speed of individual motor depends on the sensor on one side
Coward mode:
  Left sensor controls Left motor
  Right sensor controls Right motor
    Ambient = sum(getLight())/3.0 # values from 3 sensors/3
    def normalize(v):
      if v > Ambient:
      v = Ambient
    return 1.0 - v/Ambient

## Slide 10: Coward and Aggressive
    L = getLight("left")
    R = getLight("right")
    motors(normalize(L), normalize(R))
Aggressive
  Left sensor controls Right motor
  Right sensor controls Left motor
Repeat as you did before now
    L = getLight(“right")
    R = getLight(“left")
    motors(normalize(L), normalize(R))
Try flashing the light on either side of the robot

## Slide 11: Mathematical Functions
Braitenberg suggests using non-monotonic mathematical functions
  Monotonic: More light, faster motor speed; or more light, slower motor speed
  Non-monotonic: the relationship is increasing in proportion to sensory input but only up to a certain point and after that it decreases
You can use exp() for ex
Bell Curve or
Gaussian Curve
f(x) = e-x2

## Slide 12: Bell Curve Behavior
    def normalize(v):
      mean = Ambient/2.0
      stddev = Ambient/6.0
      if v >= Ambient:
        v = Ambient
    return exp(-(v - mean)**2 / 2*(stddev**2))
Other mathematical functions using math library (from math import *):
  Step
  Threshold

## Slide 13: Multiple Sensing
Adding more sensors makes the robot behavior more interesting
Scribbler in addition to light sensors has
  Stall Sensors (detect if the robot has stopped)
  IR sensors and more
Digital Sensors: Give either On or Off (e.g Stall)
Try this:
  Replace the light sensors with obstacle sensors and try moving the robot

## Slide 14: Exercise
How would you design paranoid, shadow fearing, behavior?
Paranoid should be capable of turning.
This can be accomplished by moving the right motor forward and moving the left motor in reverse direction at the same time.
Notes: It has a single threshold light sensor. When the sensor detects light, it moves forward. When the sensor enters a shadow, it reverses the direction of its left motor, thus turning right. Soon the sensor will swing around, out of the shadow. When that happens, it resumes its forward motion.

## Slide 15: If - else
    if <condition>:
    <this>
    else:
    <that>
Else if : elif
    if <condition-1>:
    <this>
    elif <condition-2>:
    <that>
    ...
    else:
    <other>
How do you use the if, else and elif
while timeRemaining(30):
if #left light is brighter that right light:
turnLeft(1.0)
else:
turnRight(1.0)
Try this:
If the left side is brighter go right, vice versa

## Slide 16: Light Follower
# Light follower
from myro import *
initialize(ask("What port?"))
# program settings...
thresh = 50
fwdSpeed = 0.8
cruiseSpeed = 0.5
turnSpeed = 0.7 # left turn, -0.7 will be right turn
def main():
while True:
# get light sensor values for left, center, and right
L, C, R = getLight()
# decide how to act based on sensor values
if C < thresh:
# bright light from straight ahead, go forward
move(fwdSpeed, 0)
elif L < thresh:
# bright light at left, turn left
move(cruiseSpeed, turnSpeed)
elif R < thresh:
# bright light on right side, turn right
move(cruiseSpeed, -turnSpeed)
else:
# no bright light, move forward slowly (or stop?)
move(cruiseSpeed/2, 0)
main()

## Slide 17: Avoiding Obstacles
# Avoiding Obstacles
from myro import *
initialize(ask("What port?"))
# program settings...
cruiseSpeed = 0.6
turnSpeed = 0.5 # this is a left turn, -0.5 will be right
turn
def main():
while True:
# get sensor values for left and right IR sensors
L, R = getIR()
L = 1 - L
R = 1 - R
# decide how to act based on sensors values
if L and R:
# obstacle straight ahead, turn (randomly)
move(0, turnSpeed)
elif L:
# obstacle on left, turn right
move(cruiseSpeed, -turnSpeed)
elif R:
# obstacle on right, turn left
move(cruiseSpeed, turnSpeed)
else:
# no obstacles
move(cruiseSpeed, 0)
main()

## Slide 18: Summary
You now have an idea of Psychology
Programming internal structures in a robot thus building brains for robot
if – else ; elseif (elif) statements